## Slide 1: Application-aware IPv6 Networking - APN6 Framework draft-li-6man-app-aware-ipv6-network-00 Zhenbin Li, Shuping Peng, Huawei Chongfeng Xie, Cong Li, China Telecom

## Slide 2
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next=43 | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Hop-by-Hop Options Header |  |  |  | 
Destination Options Header |  |  |  | 
Routing Header/SRH |  |  |  | 
…… |  |  |  | 
Destination Options Header |  |  |  | 
Payload |  |  |  | 
SRv6 SRH: Three Levels of Programmable Space
IPv6 Extension Headers
Segment [0]
Segment [1]
…
Segment [n]
Option TLV
DA
SA
IPv6 Header
SR Header
Loc
Func
Args
x
y
z
128bits
128 bits
Payload
128 bits
128 bits
128 bits
IP Header
SRv6 Segment Routing Header
TLV
Foundations for APN6 -
IPv6/SRv6 Benefits: Future-proof Programmability
1
2
3

## Slide 3
Application-aware IPv6/SRv6 Networking (APN6)
https://tools.ietf.org/html/draft-li-6man-app-aware-ipv6-network-00 @IETF105
Make use of IPv6 extensions header to convey the service requirements along with the packet to the network
To facilitate the service deployment and network resource adjustment to guarantee SLA for applications
2B
2C
Aggregation
DC
Access
ACC
AGG
AGG
ASBR
ASBR
ACC
DC GW
DC GW
Spine
Spine
Leaf
Leaf
Leaf
Leaf
APP
APP
Multi VM VNF
SRv6 (Network-side Solution)
CPE
RG
APP
APP
SRv6 (Host-side Solution)
APP
APP
IPv6 H
HBH
IPv6 H
APP Info
IPv6 H
APP Info
IPv6 H
SID List
SRH TLV
Video from Netflix/Youtube APP
/ Game from Tencent APP
IPv6 H
APP Info
IPv6 H
SID List
SRH TLV
Performance Guarantee
for applications
IPv6 H
App Info
IPv6 H
HBH
Video from Netflix/Youtube APP
/ Game from Tencent APP
SLA
User ID
APP ID
SLA
User ID
App Req. Para.
App Req. Para.
Steer into a SRv6 tunnel
App Info is added into the IPv6 EXH
App Info is carried in the SID Argus or SRH TLV
App Info is carried in the SID Argus or SRH TLV
App Info is added into the IPv6 EXH
APP ID
App-aware-process Head-End
Match to the SR policy according to the application requirements
Service-aware Apps
IPv6 enabled APP
Add ID/req. in the IPv6 EXH
App-aware-process Mid-point
Service requirements guarantee
App-aware-process End-Point
Remove the service requirements of the APPs
App-aware Edge Device (DL)
Application Identification
Add ID/req. in the IPv6 EXH
App-aware Edge Device (UL)
Application Identification
Add ID/req. in the IPv6 EXH
Service-aware Apps
IPv6 enabled APP
Add ID/req. in the IPv6 EXH
APP
MBB
FBB

## Slide 4: App-aware IPv6 Networking (APN6) Framework
APN6 is to make use of IPv6 Extension Headers
  to convey the application related information including its requirements along with the packet to the network
  to facilitate the service deployment and guarantee SLA
Optionally add the app information (ID, service requirements) in an IPv6 extension header
Optionally add the app information (ID, service requirements) in an IPv6 extension header.
Derived from L2 QinQ Info
According to the carried App Info, steer the packets into an existing path/policy, or trigger to set up new
App Info is copied to the outer IPv6 extension header
According to the carried App Info, adjust the resources locally to guarantee SLA

## Slide 5: Application-aware Options
Application-aware ID option
Service-Para Option

## Slide 6: Application-aware ID Option
Carrying application ID, user ID, flow ID, and service requirements/SLAs
The length of the APP-aware ID depends on the locations
  128bits = IPv6 address = SRv6 SID = A address
Structure I: Any combination of SLA level (e.g. Gold, Silver, Bronze), APP ID, and/or user ID, and/or Flow ID
Structure II: Any combination of SLA level (e.g. Gold, Silver, Bronze), APP ID, and/or user ID, and/or Flow ID, plus the arguments which indicating the service requirements of the identified application
Structure III: An SRv6 SID, with its arguments as the information specified in Structure II

## Slide 7: Service-Para Option
Carrying the service requirement parameter

## Slide 8: Locations for Application-aware Options
IPv6 Header [RFC8200]
IPv6 Header
Hop-by-Hop Options header
Destination Options header
Routing header
Other headers
Upper-Layer header
draft-ietf-6man-segment-routing-header

## Slide 9: Use cases What we can do with the App-aware options?
Steer packets into SRv6 tunnels/Policy at the head-end
Steer packets into the path that can guarantee SLA at the mid-point
Filter packets at VAS devices along the SFC instead of using DPI and 5 tuples
Head-end
End-Point
Low latency
High bandwidth
High reliability
Head-end
End-Point
High SLA
Low SLA
Mid-Point
Classifier
SFF2
SFF1
SF

## Slide 10: Thank you!

## Slide 11: IPv6 Enhanced HBH Options Header
The App-aware options can be carried in the HBH header, but needs to be processed at wire speed to achieve high forwarding performance
However, [RFC8200] specifies that
  nodes may be configured to ignore the Hop-by-Hop Options header (HBH)
  the packets containing a HBH may be dropped
  the packets containing a HBH may be assigned to a slow processing path, which will greatly reduce the forwarding performance
The App-aware options will not be properly processed according to the current specifications
Will it be solved only by configuration?
  All the HBH options will be treated in the same way, however, they may have different processing requirements
    https://www.ietf.org/archive/id/draft-ietf-6man-hbh-header-handling-03.txt
  Every option needs to be checked one by one and decide how to process against the pre-configuration
Or by defining a new HBH header?
  All the HBH options carried in this header will be processed at wire speed
  This header can also be used to carry the path service instruction part
IPv6 Header [RFC8200]
IPv6 Header
Hop-by-Hop Options header
Destination Options header
Routing header
Other headers
Upper-Layer header