## Slide 1: DetNet SRv6 Data Plane Encapsulation
Xuesong Geng (gengxuesong@huawei.com)
Mach Chen (mach.chen@huawei.com)
Yongqing Zhu (zhuyq.gd@chinatelecom.cn)
draft-geng-dp-sol-srv6-01

## Slide 2: DetNet Overview
Key Features
  DetNet provides a capability to carry specified unicast or multicast data flows for real-time applications with extremely low data loss rates and bounded latency within a network domain.
Key Technologies
  Resource Allocation / Service Protection / Explicit Route

## Slide 3: DetNet SRv6 Data Plane Requirement
A method of identifying the SRv6 payload type; (e.g., DSCP)
A suitable explicit route to deliver the DetNet flow ; (e.g., Segment List in SRH)
A method of indicating packet processing, such as PREOF; (detailed in next slides)
A method of identifying the DetNet flow; (detailed in next slides)
A method of carrying DetNet sequence number; (detailed in next slides)
A method of carrying queuing and forwarding indication to do congestion protection; (not covered in the current version)

## Slide 4: DetNet SRv6 Data Plane Solution
Flow Identification(20bits) and Sequence Number(28bits) are carried in:
Option1: SRH TLVs
Opiton2 : arguments in the SID for Relay Node
Option3: DetNet SID in segment list
1
2
3

## Slide 5: SRv6 Based PREOF
Ingress
Relay Node 1
[Replication]
Egress
SRv6
IPv6
IPv6
End Station 1
End Station
2
Relay Node 2
[Elimination]
Transit Node 1
Transit Node 2
IPv6 Header
IPv6 Header
SRH 1
IPv6 Header 1
SRH1
IPv6 Header 1
IPv6 Header
SRH 2
IPv6 Header 2
IPv6 Header
SRH 3
IPv6 Header 3
IPv6 Header
SRH 4
IPv6 Header 4
IPv6 Header
SRH 4
IPv6 Header 4
IPv6 Header
IPv6 Header

## Slide 6
Thanks

## Slide 7: SRv6 Data Plane Solution Option1-Encapsulation
IPv6 Header
SRH
IPv6 Header
Payload
SID for Relay Node
Type: 8bits, to be assigned by IANA.
Length: 8.
RESERVED: 28 bits, MUST be 0 on transmission and ignored on receipt.
Flow Identification: 20 bits, which is used for identifying DetNet flow.
Type: 8 bits, to be assigned by IANA.
Length: 8.
RESERVED: 20 bits. MUST be 0 on transmission and ignored on receipt.
Sequence Number: 28 bits, which is used for indicating sequence number of a DetNet flow.
Flow Identification(32bits) and Sequence Number(32bits) are carried as TLVs

## Slide 8: SRv6 Data Plane Solution Option1-Replication Function
End. B.Replication: Packet Replication Function
  IF NH=SRH & SL>0 THEN
  extract the DetNet TLV values from the SRH
  create two new outer IPv6+SRH headers: IPv6-SRH-1 and IPv6-SRH-2 Insert the policy-instructed segment lists in each newly created SRH (SRH-1 and SRH-2). Also, add the extracted DetNet TLVs into SRH-1 and SRH-2.
  remove the incoming outer IPv6+SRH header.
  create a duplication of the incoming packet.
  encapsulate the original packet into the first outer IPv6+SRH header: (IPv6-SRH-1) (original packet)
  encapsulate the duplicate packet into the second outer IPv6+SRH header: (IPv6-SRH-2) (duplicate packet)
  set the IPv6 SA as the local address of this node.
  set the IPv6 DA of IPv6-SRH-1 to the first segment of the SRv6 Policy in of SRH-1 segment list.
  set the IPv6 DA of IPv6-SRH-2 to the first segment of the SRv6 Policy in of SRH-2 segment list.
  ELSE
  drop the packet

## Slide 9: SRv6 Data Plane Solution Option1-Elimination Function
End. B. Elimination: Packet Elimination Function
  IF NH=SRH & SL>0 & "the packet is not a redundant packet" THEN
  do not decrement SL nor update the IPv6 DA with SRH[SL]
  extract the value of DetNet TLVs from the SRH
  create a new outer IPv6+SRH header
  insert the policy-instructed segment lists in the newly created SRH and add the retrieved DetNet TLVs in the newly created SRH
  remove the incoming outer IPv6+SRH header.
  set the IPv6 DA to the first segment of the SRv6 Policy in the newly created SRH
  ELSE
  drop the packet

## Slide 10: SRv6 Data Plane Solution Option2-Encapsulation
Flow Identification(20bits) and Sequence Number(28bits) are carried as arguments in the SID for Relay Node
IPv6 Header
SRH
IPv6 Header
Payload
Location & Function: the 80 most significant bits that are used for routing
Flow Identification: 20 bits, which is used for DetNet flow identification in the DetNet relay node;
Sequence Number: 28 bits, which are used for dis crime packets in the same DetNet flow;
SID for Relay Node

## Slide 11: SRv6 Data Plane Solution Option3-Encapsulation
IPv6 Header
SRH
IPv6 Header
Payload
Flow Identification and Sequence Number are carried as in DetNet SID
SID for Relay Node
SID for DetNet

## Slide 12: DetNet SRv6 Data Plane Solution Example
In
R1
R2
SRv6
IPv6
IPv6
End Station 1
End
Station 2
T2
T3
T1
T4
Eg
(In,T1)
(R1,T1;SL=2)
(ES1,ES2)
(In,R1)
(ES1,ES2)
(R1,T2)
(R2,T2;SL=2)
(ES1,ES2)
(ES1,ES2)
(ES1,ES2)
(R1,T1;SL=1)
(R2,T4)
(Eg,T4;SL=2)
(ES1,ES2)
(R1,T3)
(R2,T3;SL=2)
(ES1,ES2)
(R1,T2)
(R2,T2;SL=1)
(ES1,ES2)
(R1,T3)
(R2,T3;SL=1)
(ES1,ES2)
(R2,Eg)
(Eg,T4;SL=1)
(ES1,ES2)